## Slide 1
FEDERAL AAN SERIES • BOOK 06 BRIEFING • FEDRAMP MODERATE
One Network, Two Voice Platforms
Federal Telecommunications Modernization — Amazon Connect, Teams Phone, and the Network Architecture That Must Support Them
Voice physics
G.114: pass/fail, not preference
Amazon Connect
.com by authorized exception
Teams Phone
GCC Moderate cloud PBX
One investment
SD-WAN fixes both at once
Date Code: 2026-07-07 15:57 ET
Draft proposal by the CSI Team (Cloud Services Infrastructure) — not yet reviewed by the SSA CIO Office, OIS, or organizational leadership. Vendor selections and timelines subject to formal review.
Notes: Framing: Book 06 establishes that the agency's two most visible telecommunications platforms — the national inbound contact center on Amazon Connect and the internal unified communications platform transitioning to Microsoft Teams Phone — share a single, solvable network problem and a single network solution. The four-chip arc across the bottom is the deck's structure: first the physics (voice quality has an internationally standardized pass/fail threshold — ITU-T G.114's 150 ms one-way ceiling — not a performance preference); then Amazon Connect (running on AWS commercial .com by a specific authorized exception documented in the ATO, with boundary obligations that must be maintained at every renewal); then Teams Phone (the correct internal telephony replacement path inside GCC Moderate, introducing no new boundary complications but identical network dependencies); and finally the punchline — one SD-WAN investment (local breakout, per-DSCP steering, active-active multipath, FEC) enables both platforms without modification. That investment does not need to be made twice. Draft-proposal status; everything scoped to FedRAMP Moderate; the Date Code identifies the version — newest code wins. Vendor sources: https://www.itu.int/rec/T-REC-G.114 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 2
FOR DECISION MAKERS
Four things to understand before any telecom decision
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
2
1
Voice has a pass/fail threshold
ITU-T G.114: one-way delay must not exceed 150 ms. Western field office agents already exceed it before a call begins under MPLS hairpin architecture. Not a preference — a ceiling.
2
Connect runs on .com by authorized exception
The exception is documented in the ATO, must be maintained at each renewal, and carries specific boundary obligations — SSP SA-9, recording storage, federation documentation.
3
Teams Phone in GCC Moderate is the correct path
No new boundary complications for internal telephony replacement — but network dependencies identical to Amazon Connect: same delay, jitter, and loss ceilings.
4
One network investment enables both
SD-WAN local breakout, per-DSCP steering, active-active multipath, and FEC apply to both platforms without modification. The investment is made once.
Why modernization must begin with voice: web apps load slowly, file transfers retransmit, meetings buffer — voice makes network problems immediately, publicly audible. Voice is the canary.
Notes: The book's executive summary, four claims: (1) Voice quality has a pass/fail threshold defined by international standard — ITU-T G.114 specifies one-way voice delay must not exceed 150 ms, and field office agents in western locations already exceed that limit before a call begins under the MPLS hairpin architecture. (2) Amazon Connect runs on AWS commercial .com by a specific authorized exception — documented in the ATO, maintained at each renewal, carrying specific boundary obligations this deck walks through. (3) Teams Phone in GCC Moderate is the correct path for internal telephony replacement — it introduces no new boundary complications, but it introduces network dependencies identical to Amazon Connect. (4) One network modernization investment enables both platforms — SD-WAN local breakout, per-DSCP steering, active-active multipath, and FEC apply to both without modification. Close on the blue bar — the canary argument, near-verbatim from the book: a web application with 200 ms of extra latency loads slowly; a file transfer with 2% loss retransmits and completes; a Teams meeting with moderate jitter buffers and recovers. A voice call with 200 ms one-way delay is barely intelligible; 2% packet loss produces audible dropouts every few seconds. Voice does not hide network problems behind buffers and retransmissions — it makes them immediately, publicly audible, to the citizen, the agent, and the supervisor on quality monitoring. That is why network modernization must begin with voice. Vendor sources: https://www.itu.int/rec/T-REC-G.114 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 3
THE FRONT DOOR TO THE AGENCY
The N8NN call journey: where quality is won or lost
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
3
1
Citizen dials
N8NN from any PSTN phone
2
AWS terminates
Voice connector into Connect (.com)
3
IVR + queue
Contact flow answers, routes
4
Agent selected
WebRTC session to agent browser
5
Voice flows
Agent ↔ agency network ↔ AWS ↔ citizen
Steps 1–3: inside AWS commercial Unaffected by the agency network. PSTN termination, IVR, queuing all happen in the Amazon Connect cloud. No agency investment changes these steps.
Step 5: the agent-to-cloud path Determined entirely by the agency's network architecture. This is where G.114 compliance is won or lost — the segment between the agent's desk and the cloud is the agency's own network, where the problem lives and the solution must be built.
Notes: The N8NN is not a telephone feature — it is the primary channel through which citizens reach the agency. Every call that fails to connect, every conversation degraded by choppy audio, every dropped session during a complex transaction represents a citizen who did not receive the service the agency exists to provide. Walk the five steps: (1) the citizen dials the N8NN from any PSTN telephone; (2) the call terminates at an AWS voice connector into Amazon Connect on AWS commercial; (3) the contact flow answers, runs the IVR, and routes to a queue; (4) an agent is selected and Connect establishes a WebRTC session to the agent's browser; (5) voice travels agent desktop → agency network → internet → AWS .com → Amazon Connect → citizen. The two panels are the operational split: steps 1 through 3 happen inside AWS commercial and are unaffected by the agency's network — no agency investment changes them. Step 5 — the agent-to-cloud path — is determined entirely by the agency's network architecture, and it is where G.114 compliance is won or lost. Behind the N8NN sits the platform, the network, and agents whose ability to hear and be heard clearly is determined entirely by the network segment between their desk and the cloud. That segment is the agency's own network: where the problem lives and where the solution must be built. Vendor sources: https://aws.amazon.com/connect/ | https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 4
THE PHYSICS OF VOICE — DELAY
ITU-T G.114: the 150 ms ceiling and what is left for the network
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
4
The 150 ms one-way budget, spent left to right:
Codec ~20 ms
Jitter buffer 50–80 ms (adaptive)
Network budget: ~50–75 ms remains
0 ms
150 ms — G.114 ceiling
FAIL
Portland agent via MPLS hairpin
One-way network latency 80–110 ms against a 75 ms budget. Over spec before any congestion. The citizen hears the degradation.
PASS
Portland agent via local DIA breakout
One-way network latency 5–15 ms to AWS us-west-2 — geographically adjacent. The physics minimum for this path, far within budget.
Above 150 ms talker echo becomes perceptible and conversation degrades. Above 400 ms the call is unusable. These are not targets — they are ceilings.
Notes: ITU-T G.114 is the international standard governing one-way delay in voice communications: one-way mouth-to-ear delay must not exceed 150 ms for most applications. Above 150 ms, talker echo becomes perceptible and conversation degrades; above 400 ms the call becomes unusable for interactive conversation. These are ceilings, not targets. Walk the budget bar left to right: the 150 ms covers the ENTIRE path — codec encoding (~20 ms for Opus), the adaptive jitter buffer at the receiver (typically 50–80 ms), and decoding — leaving approximately 50–75 ms of budget for the network itself. That network budget is the engineering target for every agent location. The two comparison cards make it concrete with the series' standing example: a Portland agent whose traffic hairpins over MPLS through Washington before internet egress reaches AWS us-west-2 with 80–110 ms one-way network latency — over spec before the call begins, and the citizen hears it. The same agent with local DIA breakout reaches us-west-2 in 5–15 ms, because Portland and us-west-2 are geographically adjacent — that is the physics minimum for the path, far within budget. No procurement decision changes the propagation delay of a Portland-to-Washington detour; the only fix is to remove the detour. Vendor sources: https://www.itu.int/rec/T-REC-G.114 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 5
THE PHYSICS OF VOICE — SCORING
MOS and the E-model: how call quality is quantified
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
5
R-Factor | MOS | Quality | User perception
90–100 | 4.3–5.0 | Excellent | Imperceptible impairment
80–90 | 4.0–4.3 | Good | Perceptible but not annoying — the N8NN floor
70–80 | 3.6–4.0 | Fair | Slightly annoying
60–70 | 3.1–3.6 | Poor | Annoying — citizen complaints begin below 3.6
Below 60 | Below 3.1 | Bad | Very annoying; many callers abandon
The operational floor: the N8NN contact center must sustain MOS above 4.0 consistently across all agent locations. Below 3.6 generates citizen complaints. Below 3.1, calls are abandoned and reported. The ITU-T G.107 E-model translates measured network conditions — delay, jitter, loss — into the R-factor, which maps to the MOS reported by call quality monitoring.
Notes: The ITU-T G.107 E-model is the standardized computational model that translates network conditions into an R-factor on a 0–100 scale, which maps to the Mean Opinion Score (MOS, 1–5) that call quality monitoring systems report. This is how the physics of the previous slide becomes a dashboard number a supervisor can watch. Walk the table: R-factor 90–100 maps to MOS 4.3–5.0, excellent, imperceptible impairment. 80–90 maps to 4.0–4.3, good, perceptible but not annoying — this teal row is the N8NN operating floor. 70–80 is fair, slightly annoying. 60–70 is poor and annoying — citizen complaints begin below MOS 3.6. Below 60 is bad — very annoying, and many callers abandon. The operational commitments to voice: the N8NN must sustain MOS above 4.0 consistently across ALL agent locations, not on average — a fleet average of 4.2 with three western offices at 2.9 is a failure hidden by arithmetic. Below 3.6 generates citizen complaints; below 3.1 calls are abandoned and reported. Phase 4 of the roadmap turns this into a per-location MOS floor SLA with alerting when sustained MOS drops below threshold — the E-model is what makes voice quality a measurable, auditable obligation rather than a subjective complaint stream. Vendor sources: https://www.itu.int/rec/T-REC-G.107 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 6
THE PHYSICS OF VOICE — VARIANCE AND LOSS
Jitter and packet loss: the other two ceilings
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
6
GOOD <30 ms jitter · MOS 4.3
JITTER 80 ms variance · MOS 3.2
LOSS 2% loss · audible gaps
time →
Jitter <30 ms — or the buffer eats the budget Jitter buffers hold packets to smooth variance — but a buffer big enough to absorb 80 ms of variance ADDS 80 ms of delay, breaching G.114. You can absorb jitter or meet the delay budget; a jittery network forces the choice.
Loss <1% — voice does not retransmit Voice RTP conceals or skips lost packets; it never retransmits. Opus handles occasional single-packet loss gracefully; consecutive losses or rates above 3% produce gaps no concealment algorithm can hide.
Notes: Delay is one of three ceilings; jitter and packet loss are the other two, and this slide shows what each sounds like. The three packet rows visualize arrival patterns: the GOOD row — ten evenly spaced packets, under 30 ms jitter, MOS 4.3. The JITTER row — the same ten packets bunched and gapped with 80 ms of variance, MOS 3.2, annoying. The LOSS row — two packets simply gone (the dashed outlines), 2% loss, audible dropouts every few seconds. The amber panel is the jitter trap worth voicing carefully: jitter buffers compensate for variance by holding packets briefly, but a buffer large enough to absorb 80 ms of variance adds 80 ms of delay — breaching the G.114 ceiling from the previous slide. You can absorb jitter or meet the delay budget; a jittery network forces the choice. That is why the requirement is jitter below 30 ms, not a bigger buffer. The red panel is the loss trap: voice RTP does not retransmit lost packets — they are concealed or skipped, never recovered. The Opus codec conceals occasional single-packet loss gracefully; consecutive losses or rates above 3% produce gaps no concealment algorithm can hide. Packet loss above 1% produces audible dropouts. Together the three ceilings — 75 ms network delay, 30 ms jitter, 1% loss — are the specification both voice platforms in this deck must meet, from every agent location. Vendor sources: https://www.itu.int/rec/T-REC-G.107 | https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 7
PLATFORM ONE — THE CONTACT CENTER
Amazon Connect: cloud-native, browser-based, no PBX
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
7
Managed SaaS contact center Inbound/outbound call handling, IVR via contact flows, skills-based routing, real-time and historical analytics, call recording — all managed service.
Browser-based agent desktop The Contact Control Panel (CCP) is a WebRTC softphone in the browser. No proprietary hardware at the desk, no on-premises call processing, no PBX to maintain.
AI-assisted operations Contact Lens: real-time transcription, sentiment analysis, supervisor alerting. Amazon Q agent assist. The capabilities that drove the platform evaluation.
The architectural consequence: with no on-premises call processing, EVERYTHING depends on the network path between the agent's browser and the AWS cloud. The platform is only as good as the segment the agency controls.
Notes: Amazon Connect is AWS's cloud-native contact center platform: inbound and outbound call handling, IVR via contact flows, skills-based routing, real-time and historical analytics, call recording, and the agent desktop — all delivered as a managed SaaS service. The three rows to walk: first, it is a managed service — there is no contact center infrastructure for the agency to operate; capacity, upgrades, and platform availability are AWS's obligation under the FedRAMP authorization. Second, the agent desktop is the Contact Control Panel — a browser-based WebRTC softphone. No proprietary hardware at the agent's desk, no on-premises call processing equipment, no PBX to maintain. Third, the AI-assisted capabilities — Contact Lens real-time transcription, sentiment analysis and supervisor alerting, plus Amazon Q agent assist — are the operational capabilities that drove the platform evaluation (and, as the next slide covers, the capability categories where .us lagged .com at evaluation time). The architectural consequence in the blue bar is the pivot for the whole deck: because nothing processes calls on premises, everything depends on the network path between the agent's browser and the AWS cloud. The platform is only as good as the segment the agency controls — which is exactly the segment the SD-WAN modernization fixes. Vendor sources: https://aws.amazon.com/connect/ | https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 8
PLATFORM ONE — THE BOUNDARY DECISION
AWS .us vs. .com: why the agency runs Connect on commercial
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
8
Provider | Moderate delivery model | Sovereign / separate model
AWS | .us infrastructure (separate government regions) | GovCloud — physically separate, screened personnel
Microsoft | Partitioned .com (GCC Moderate on Azure Commercial) | Physically separate sovereign offerings
Oracle | Partitioned .com (OCI Moderate) | OCI Government Cloud (separate)
Capability gaps in .us Connect at evaluation time — the reason for the exception:
AI-assisted capabilities Contact Lens and Amazon Q agent assist availability lagged
Integration ecosystem Marketplace CRM/WFM integrations certified for commercial
Tooling and support maturity Feature release cadence in .us lagged commercial
Current evaluation required before any NEW deployment: AWS continuously updates .us. The gaps identified at evaluation time may have closed — re-evaluate .us Connect against requirements before concluding a .com exception is necessary.
Notes: AWS structures its federal cloud offerings differently from Microsoft and Oracle, and the table makes the comparison: AWS delivers its Moderate baseline on .us infrastructure — separate government regions — with GovCloud as the physically separate, screened-personnel sovereign model. Microsoft delivers GCC Moderate as a partition of Azure Commercial (.com), with physically separate sovereign offerings above it. Oracle mirrors that pattern with OCI Moderate on partitioned .com. Amazon Connect is available on .us. At the time the agency evaluated platforms for the N8NN, the .us version presented operational capability gaps relative to commercial .com in three categories — the amber cards: AI-assisted contact center capabilities (Contact Lens real-time transcription, sentiment analysis, supervisor alerting, and Amazon Q agent assist availability lagged); the third-party integration ecosystem (AWS Marketplace integrations for CRM connectors, workforce management, and reporting were predominantly certified for commercial Connect); and operational tooling and support maturity (support procedures and feature release cadence in .us lagged commercial). The red bar is the standing caveat, near-verbatim from the book: AWS continuously updates its .us infrastructure, and the capability gaps identified at this agency's evaluation may have closed. Any agency evaluating Connect for a NEW deployment must conduct a current-state evaluation of .us Connect against its specific requirements before concluding that a .com exception is necessary. The exception is a documented evaluation outcome, not a default. Vendor sources: https://aws.amazon.com/connect/ | https://aws.amazon.com/compliance/fedramp/ | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 9
PLATFORM ONE — THE EXCEPTION, STRUCTURALLY
The .com exception: same pattern as GCC Moderate
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
9
What it IS
A federally authorized service on commercial infrastructure with FedRAMP Moderate controls applied
The same structural pattern as GCC Moderate on Azure Commercial
US-based data centers; encryption in transit and at rest
Amazon Connect holds FedRAMP Moderate authorization
What it is NOT
Not GovCloud: the personnel screening, physical separation, and elevated baseline of GovCloud do not apply
Not a permanent waiver: time-bounded, condition-bounded, reviewed at each ATO renewal
Not less secure by definition — FedRAMP Moderate controls are extensive
Not invisible: the boundary must be accurately reflected in the SSP and understood by the AO
The obligation the exception creates: the authorization boundary is explicitly a commercial environment with federal controls applied. That boundary must be accurately reflected in the SSP, understood by the AO, and re-evaluated at each authorization renewal — including whether the .us capability gaps that justified it still exist.
Notes: This slide keeps the exception from being misread in either direction. The agency's use of Amazon Connect on AWS commercial .com is the same structural pattern as GCC Moderate on Azure Commercial: a federally authorized service running on commercial infrastructure with FedRAMP Moderate controls applied. AWS commercial data centers are US-based; data is encrypted in transit and at rest; Amazon Connect holds FedRAMP Moderate authorization. For an audience that has internalized the series' GCC Moderate boundary discussion, this is a familiar shape, not an anomaly. What it is NOT: it is not GovCloud — the personnel screening, physical separation, and elevated control baseline of GovCloud do not apply. It is not a permanent waiver — the specific authorization permitting .com Connect is time-bounded and condition-bounded, and requires active maintenance at each ATO renewal. It is not less secure by definition — FedRAMP Moderate controls are extensive. And it is not invisible — the boundary must be accurately reflected in the SSP and understood by the Authorizing Official. The blue bar is the obligation: the authorization boundary is explicitly a commercial environment with federal controls applied, re-evaluated at each renewal — including whether the .us capability gaps that justified the exception still exist. Phase 4 of the roadmap makes that re-evaluation a standing ConMon item rather than a scramble at renewal time. Vendor sources: https://aws.amazon.com/compliance/fedramp/ | https://www.fedramp.gov/20x/ | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 10
THE NETWORK PROBLEM
The MPLS hairpin applied to the N8NN: before and after
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
10
BEFORE — the hairpin
Portland agent → MPLS → Washington → internet → AWS us-west-2 → Connect
One-way network latency: 80–110 ms
G.114 network budget: 75 ms — OVER SPEC
The traffic travels ~2,400 miles east to reach a cloud region ~170 miles from the agent
The citizen hears the degradation on every call
AFTER — local breakout
Portland agent → local DIA → AWS us-west-2 → Connect
One-way network latency: 5–15 ms
Far within the 75 ms budget
Portland and us-west-2 are geographically adjacent — this is the physics minimum
MPLS is retained for on-premises VMware workloads
Bandwidth does not fix this: the hairpin is a distance problem, not a volume problem. No circuit upgrade changes the propagation delay of a 4,800-mile round-trip detour. The fix is removing the detour.
Notes: The MPLS hairpin, applied specifically to the N8NN contact center. BEFORE: an agent in Portland whose network routes all internet traffic through Washington before egress reaches AWS us-west-2 by traveling Portland → MPLS → Washington → internet → back across the country to us-west-2 → Amazon Connect. One-way network latency: 80 to 110 ms against a G.114 network budget of 75 ms. Over spec — before any congestion, before any inspection queueing. The citizen hears the degradation on every call, and the supervisor sees it in the MOS reports. The absurdity to voice: the traffic travels roughly 2,400 miles east to reach a cloud region that is about 170 miles from the agent. AFTER: the same agent with local internet breakout — Portland → local DIA → AWS us-west-2 → Connect. One-way network latency: 5 to 15 ms, because Portland and us-west-2 are geographically adjacent. This is the physics minimum for the path, far within budget. Note the retained role for MPLS: it continues carrying traffic to on-premises VMware workloads — local breakout is additive, not a rip-and-replace. The blue bar is the recurring series point, stated for telecom: bandwidth is volume, latency is distance. The hairpin is a distance problem, and no circuit upgrade changes the propagation delay of a 4,800-mile round-trip detour. The fix is removing the detour — which is what SD-WAN local breakout does, per application, under policy. Vendor sources: https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 11
THE ENGINEERING SPECIFICATION
WebRTC network requirements: the numbers the network must hit
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
11
Parameter | Requirement | Notes
One-way delay | ≤75 ms network budget | G.114 limit minus codec and jitter buffer overhead
Jitter | <30 ms | Above this, buffer compensation breaches the delay budget
Packet loss | <1% | Above 1% audible; above 3% unintelligible
Bandwidth per agent | ~100 Kbps | Opus codec including RTP overhead
Protocol | RTP/SRTP over UDP | TCP fallback degrades quality; avoid
DSCP marking | EF (46) | SD-WAN must honor, not remark
NAT traversal | STUN/TURN | Direct UDP preferred; TURN relay adds latency
Firewall | UDP 3478, 443 outbound | Must reach AWS .com endpoints without hairpin inspection delay
These same numbers govern Teams Phone. One specification, two platforms — measure it per agent location before any migration.
Notes: The engineering specification in one table — the numbers the agency network must hit for the browser-based WebRTC softphone, drawn from the book's requirements table and AWS's Contact Control Panel networking guidance. Walk the load-bearing rows: one-way delay at or under 75 ms of network budget — that is the G.114 150 ms ceiling minus codec and jitter buffer overhead. Jitter under 30 ms — above that, the buffer compensation needed to smooth it breaches the delay budget (the trap from the physics section). Packet loss under 1% — audible above that, unintelligible above 3%. Bandwidth is trivial — about 100 Kbps per agent with Opus including RTP overhead; voice is never a bandwidth problem, which is exactly why buying bandwidth never fixes it. Protocol: RTP/SRTP over UDP — TCP fallback exists but degrades quality and should be treated as a failure indicator, not a working mode. DSCP EF (46) marking — and the note matters: the SD-WAN must HONOR the marking, not remark it. NAT traversal via STUN/TURN with the direct UDP path preferred — a TURN relay adds latency. Firewall: UDP 3478 and 443 outbound must reach AWS .com endpoints without hairpin inspection delay. The bottom bar is the deck's refrain: these same numbers govern Teams Phone. One specification, two platforms — and Phase 1 of the roadmap measures it per agent location before any migration proceeds. Vendor sources: https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | https://www.itu.int/rec/T-REC-G.114 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 12
THE SECOND FAILURE MODE
Asymmetric routing: the session killer latency does not explain
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
12
Agent
SYN out
Stateful firewall A
session entry created ✓
Stateful firewall B
SYN-ACK, no entry → DROPPED
AWS / GCC
SYN-ACK back
outbound path
return path — different route
The fix SD-WAN tunnel: one logical connection, stateful inspection at the endpoint sees both directions. Asymmetry below the tunnel becomes structurally invisible.
Why it matters for voice: the CCP session setup and Teams SIP signaling are TCP-based. If the request goes through one stateful device and the response through another, the session fails before audio is ever established. And it masquerades: the agent reports "the phone system is broken"; the Teams failure is blamed on "SBC misconfiguration." The diagnostic requires capturing TCP session establishment and verifying both directions traverse the same stateful devices.
Notes: The second, independent failure mode — the one latency numbers do not explain. Asymmetric routing occurs when a session's outbound path and return path traverse different stateful devices. Walk the diagram: the agent's SYN goes out through stateful firewall A, which creates a session table entry expecting the return through it. The SYN-ACK comes back from AWS or the GCC edge via a different path — firewall B — which has no session entry and drops it as unsolicited. TCP never completes; the call never connects — with PERFECT latency on every individual link. Why it matters for both voice platforms: the HTTPS session setup for Amazon Connect's Contact Control Panel is TCP-based, and Teams Phone call setup rides SIP signaling — if the request goes through one stateful device and the response through another, the session fails before audio is ever established. The masquerade is the operational trap, near-verbatim from the book: an agent whose Connect sessions fail will report 'the phone system is broken'; a Teams Phone failure at SIP signaling will be attributed to 'SBC misconfiguration.' The diagnostic path requires capturing TCP session establishment and verifying both directions traverse the same stateful devices — expensive, per-incident forensics. The teal panel is the structural fix: the SD-WAN tunnel is a single logical connection between two edge devices; stateful inspection happens at the tunnel endpoint, which sees both directions. Asymmetric physical routing below the tunnel is structurally invisible to the application — the failure mode is eliminated by architecture, not by per-incident troubleshooting. Vendor sources: https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 13
PLATFORM TWO — INTERNAL TELEPHONY
Teams Phone: the cloud PBX inside GCC Moderate
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
13
Cloud PBX in the Teams client Extension dialing, voicemail, transfer, call queues, auto attendants, PSTN connectivity — replacing the on-premises telephone system, delivered through the client agents already run.
Inside the existing boundary Operates within GCC Moderate — same FedRAMP Moderate authorization, data residency, and feature availability constraints as the rest of the agency's M365 environment. No new boundary complications.
Same audio path as Teams meetings A Teams Phone call and a Teams meeting use the same client, the same audio path, the same DSCP EF marking, the same dependency on low-latency connectivity to GCC infrastructure.
The consequence: fixing the network for Teams meetings fixes it for Teams Phone simultaneously. The Book 05 SD-WAN work and this book's telephony work are the same investment.
Notes: Platform two. Microsoft Teams Phone is the cloud PBX capability within Microsoft 365 that enables Teams to replace a traditional on-premises telephone system: extension dialing, voicemail, call transfer, call queues, auto attendants, and PSTN connectivity — all delivered through the Teams client agency staff already run every day. The three rows: first, it is a full PBX replacement in the client — no new application, no new interface for staff to learn beyond the dial pad appearing in Teams. Second, the boundary story is clean: Teams Phone operates within GCC Moderate, subject to the same FedRAMP Moderate authorization, data residency requirements, and feature availability constraints as the rest of the agency's Microsoft 365 GCC environment. Unlike Amazon Connect, there is no exception to document — this is why the exec summary calls Teams Phone 'the correct path' for internal telephony: it introduces no new boundary complications. Third — the architecturally decisive point — Teams Phone is not a separate audio stack: an agent answering a Teams Phone call and an agent joining a Teams meeting use the same client, the same audio path, the same DSCP EF marking for audio streams, and the same network dependency on low-latency, low-jitter connectivity to Microsoft's GCC infrastructure. The teal bar draws the conclusion: fixing the network for Teams meetings fixes it for Teams Phone simultaneously. The Book 05 SD-WAN and M365 optimization work and this book's telephony modernization are the same investment — which is the deck's one-investment thesis appearing for the second time. Vendor sources: https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | https://learn.microsoft.com/en-us/office365/servicedescriptions/office-365-platform-service-description/office-365-us-government/gcc | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 14
PLATFORM TWO — REACHING THE PHONE NETWORK
PSTN connectivity: Calling Plans, Direct Routing, and the SBC
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
14
Microsoft Calling Plans
Microsoft provides PSTN connectivity as a licensed add-on
Simplest operational model — no SBC to run
Confirm availability in GCC Moderate for the agency's geographic footprint and number types BEFORE committing
Direct Routing (SBC)
Agency connects its PSTN carrier via a Microsoft-certified Session Border Controller
SBC terminates carrier SIP trunks, presents them to Teams
Natural candidates given existing Cisco voice estate: Cisco CUBE, or an AudioCodes / Ribbon-class cloud SBC
SBC deployment — two viable models: On-premises at the Washington data center — familiar operational model, but ALL PSTN traffic from every agent location hairpins through it, and it is a single point of failure. Cloud SBC hosted by the vendor — geographically distributed, multiple PoPs, removes the single point of failure.
Procurement gate: a cloud SBC used with a FedRAMP Moderate system must itself hold FedRAMP authorization at the Moderate baseline or above — confirm on the Marketplace before procurement.
Notes: Connecting Teams Phone to the public switched telephone network requires one of two approaches. Microsoft Calling Plans: Microsoft provides PSTN connectivity as a licensed add-on — the simplest operational model with no SBC to operate, but availability in GCC Moderate must be confirmed for the agency's specific geographic footprint and number types before committing to this path. Direct Routing: the agency connects its own PSTN carrier to Teams Phone via a certified Session Border Controller — the SBC terminates SIP trunks from the carrier and presents them to Teams via a Microsoft-certified SIP interface. For an agency operating existing Cisco voice infrastructure at data center locations, a Cisco CUBE or a cloud-hosted SBC from an AudioCodes or Ribbon-class vendor are the natural candidates. The SBC deployment question in the grey panel: an on-premises SBC at the Washington data center is the familiar operational model, but every PSTN call from every agent location hairpins through it — re-creating for telephony the exact pattern this series exists to eliminate — and it is a single point of failure for all inbound and outbound PSTN calling. A cloud SBC hosted in the vendor's cloud is geographically distributed with multiple PoPs and removes the single point of failure. The amber procurement gate, verbatim in substance from the book: a cloud SBC used with a FedRAMP Moderate system must itself hold FedRAMP authorization at the Moderate baseline or above — confirm the vendor's current status on the FedRAMP Marketplace before procurement, not after. Vendor sources: https://learn.microsoft.com/en-us/microsoftteams/direct-routing-landing-page | https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 15
PLATFORM TWO — THE LEGAL FLOOR
E911: two federal laws, one go-live gate
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
15
Kari's Law (2018)
Users must dial 911 directly — no access code, no prefix
Notification to a central point when 911 is dialed
Teams Phone satisfies both when emergency calling policies are correctly configured
Ray Baum's Act (2018)
"Dispatchable location" must go to the PSAP with the call
Not just a building address: floor, room, workstation
Teams supports it via Location Information Service (LIS) + ELIN configuration
E911 is not optional — 47 CFR Part 9. Per location before go-live:
(1) configure the LIS entry with dispatchable location · (2) configure the emergency calling policy routing to the correct PSAP · (3) test 911 dialing and callback from a representative device · (4) document the test in the deployment record.
Remote workers: location awareness policy must capture the remote worker's current location at sign-in — the dispatchable-location obligation follows the person, not the building.
Notes: The legal floor under any multi-line telephone system, including a cloud PBX. Two federal laws: Kari's Law (2018) — users must be able to dial 911 directly without an access code or prefix, and a notification must be sent to a central point when 911 is dialed; Teams Phone satisfies both requirements when emergency calling policies are correctly configured. Ray Baum's Act (2018) — the 'dispatchable location,' not just a building address but the specific floor, room, or workstation, must be transmitted with the 911 call to the Public Safety Answering Point; Teams Phone supports dispatchable location via the Location Information Service (LIS) and Emergency Location Identification Number (ELIN) configuration. The red panel is the go-live gate, and it is regulatory, not advisory — E911 compliance is a federal legal requirement under 47 CFR Part 9. For each location where Teams Phone will be activated, the agency must: configure a Location Information Service entry with dispatchable location; configure an emergency calling policy that routes to the correct PSAP; test 911 dialing and callback from a representative device at that location; and document the test in the deployment record. Four steps, per location, before go-live — this is why the Phase 3 roadmap carries E911 validation as an explicit line item rather than a footnote. The amber panel flags the hard case: remote workers. The location awareness policy must capture the remote worker's current location at sign-in — the dispatchable-location obligation follows the person, not the building, and a hybrid workforce makes this a standing operational process rather than a one-time configuration. Vendor sources: https://www.fcc.gov/mlts-911-requirements | https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 16
PLATFORM TWO — THE TRANSITION
Legacy PBX migration: tranches, parallel operation, and the fax problem
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
16
1
Port in geographic tranches
One field office region at a time — never a single nationwide cutover. Each tranche is a bounded, reversible event.
2
Run in parallel
Legacy PBX and Teams Phone operate side by side through the transition. Ported numbers route to Teams; un-ported numbers still reach the legacy system.
3
Rebuild routing logic
Legacy hunt groups become Teams Call Queues; auto attendant menus are recreated as Teams Auto Attendants — inventoried and mapped before each tranche.
4
Handle fax separately
Analog fax lines cannot ride Teams Phone. Inventory them; solve with fax-over-IP or a cloud fax service on a separate track from voice porting.
What staff gain: voicemail transcription, auto attendants, call queues, mobile calling — with no proprietary desk hardware and no per-seat PBX licensing. The migration is a platform upgrade, not a like-for-like swap.
Notes: The transition mechanics — four disciplines that keep a PBX replacement from becoming an outage. First, port numbers in geographic tranches: one field office region at a time, never a single nationwide cutover. Each tranche is a bounded, reversible event with its own validation — and this pairs with the roadmap's rule that no office migrates before its network is G.114-validated. Second, parallel operation: during the transition the legacy PBX and Teams Phone must operate side by side — calls to ported numbers route correctly to Teams while calls to un-ported numbers still reach the legacy system; the routing split is per-number, not per-site. Third, rebuild the routing logic: legacy PBX hunt groups must be recreated as Teams Call Queues, and auto attendant menus recreated as Teams Auto Attendants — which requires inventorying what the legacy system actually does before each tranche, since decades-old hunt group configuration is rarely documented. Fourth, the fax problem: legacy analog fax lines cannot be replaced by Teams Phone — they need a fax-over-IP solution or a cloud fax service, so the inventory must classify every legacy number as voice, fax, emergency, or special service, and fax gets handled on a separate track from voice porting. The blue bar frames the outcome positively for staff: voicemail transcription, auto attendants, call queues, and mobile calling arrive with the migration, with no proprietary desk hardware and no per-seat PBX licensing — a platform upgrade, not a like-for-like swap. Vendor sources: https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | https://learn.microsoft.com/en-us/microsoftteams/direct-routing-landing-page | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 17
THE CONVERGENCE
One investment, two platforms: the same network fixes both
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
17
Amazon Connect
AWS .com — citizen calls
Teams Phone
GCC Moderate — internal + PSTN
SD-WAN / AAN local breakout · DSCP EF steering · multipath · FEC
Agent workstation
field office / telework
Shared requirement, both platforms: <75 ms one-way · <30 ms jitter · <1% loss · DSCP EF honored end to end
Not just a DIA circuit: Application-Aware Networking — policy by application identity, user identity, device posture, and behavior. Not source IP and port alone.
Notes: The convergence slide — the deck's thesis in one picture. Both Amazon Connect and Teams Phone are cloud SaaS voice platforms; both generate real-time RTP/SRTP streams; both are broken by the same MPLS hairpin and repaired by the same network solution. The hub is that solution: SD-WAN with local breakout, per-DSCP steering, active-active multipath, and FEC — one investment serving the citizen-facing contact center on AWS .com and the internal cloud PBX in GCC Moderate simultaneously, down to the same agent workstation at the bottom. The grey bar is the shared specification, identical for both platforms: under 75 ms one-way network delay, under 30 ms jitter, under 1% packet loss, with DSCP EF honored end to end. One specification, one network, two platforms — the investment does not need to be made twice. And the italic line above the diagram carries the series' definitional point: the solution is not simply 'add a DIA circuit.' It is Application-Aware Networking — a network architecture in which policy decisions, path selection, security enforcement, and traffic treatment are determined by the full context of a transaction: application identity, user identity, device posture, and behavioral characteristics, not by source IP and port alone. The bare-pipe distinction gets its own treatment three slides ahead, where DIA-without-controls meets the NIST control table. Vendor sources: https://aws.amazon.com/connect/ | https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 18
THE CONVERGENCE — AT ONE DESK
The hybrid agent: two simultaneous DSCP EF streams
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
18
Agent workstation Connect CCP (browser)
+ Teams desktop client
— both on active calls
Stream 1 — citizen call Connect WebRTC → AWS .com · DSCP EF · ~100 Kbps
Stream 2 — supervisor call Teams Phone → GCC Moderate · DSCP EF · ~100 Kbps
Capacity planning formula: (max concurrent hybrid agents) × 200 Kbps = reserved DSCP EF capacity on the lowest-latency path. A field office with 20 concurrent hybrid agents needs 4 Mbps of protected EF capacity at peak.
Standardize the endpoints too: run Connect's CCP in a Chromium browser and Teams as the desktop client (avoids compatibility edge cases); standardize headsets across the agent population before go-live — ad hoc headset choices create support complexity and audio inconsistency that confounds troubleshooting.
Notes: The convergence at a single desk. When an agent has an active Amazon Connect call with a citizen and simultaneously receives a Teams Phone call — a supervisor consult, an internal transfer — the workstation is generating two concurrent voice streams, both marked at the highest QoS priority, DSCP EF. Stream 1: the citizen call via Connect WebRTC to AWS .com, about 100 Kbps. Stream 2: the Teams Phone call to GCC Moderate, another 100 Kbps. Both must ride the lowest-latency path simultaneously, and the SD-WAN per-DSCP policy must provide enough protected bandwidth for both. The amber panel is the sizing rule to take away, verbatim from the book: maximum concurrent hybrid agents × 200 Kbps = reserved DSCP EF capacity on the lowest-latency path. At a field office with 20 concurrent hybrid agents that is 4 Mbps of DSCP EF traffic that must be accommodated at peak — a small number, but one that must be RESERVED, not left to contend with bulk traffic. This lands in Phase 1 of the roadmap as an explicit sizing step. The grey panel covers the endpoint discipline that keeps troubleshooting sane: Amazon Connect's Contact Control Panel is optimized for Chromium-based browsers while Teams Phone is optimized for the Teams desktop client — running Connect in Chrome and Teams as the desktop client avoids browser compatibility edge cases; and headset configuration must be standardized across the agent population before go-live on both platforms, because ad hoc headset choices create support complexity and inconsistent audio quality that confounds network troubleshooting — a MOS complaint that is actually a headset is wasted network forensics. Vendor sources: https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 19
THE CONVERGENCE — TRAFFIC CLASSES
Per-DSCP steering: three classes from one workstation
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
19
Amazon Connect voice — DSCP EF Citizen call audio. Lowest-latency path, unconditionally. FEC enabled if path loss ≥0.5%.
Teams Phone voice — DSCP EF Supervisor or internal call audio. Same lowest-latency path, same protections.
CCP web app + Teams UI — HTTPS The browser and application interfaces. Highest-throughput path — they tolerate 200–500 ms without affecting call quality and must not compete with voice for the latency-sensitive path.
Why this is the AAN argument in miniature: one workstation, three traffic classes, three different correct treatments — decided per application, not per circuit. A network that treats all three identically fails voice to protect web traffic that never needed protecting.
Notes: The hybrid agent workstation generates three simultaneous traffic classes during active calls, and each needs a different treatment. Class one: Amazon Connect voice, marked DSCP EF — citizen call audio, steered to the lowest-latency path unconditionally, with forward error correction enabled on any path with measured loss at or above 0.5%. Class two: Teams Phone voice, also DSCP EF — supervisor or internal call audio, riding the same lowest-latency path with the same protections. Class three: the Contact Control Panel web application and the Teams user interface — ordinary HTTPS that tolerates 200 to 500 ms of latency without any effect on call quality, steered to the highest-throughput path precisely so it does not compete with voice for the latency-sensitive path. The blue bar makes this the series thesis in miniature, and it is worth pausing on: one workstation, three traffic classes, three different correct treatments — decided per application, not per circuit. A network that treats all three identically — the flat-QoS legacy posture — fails voice in order to protect web traffic that never needed protecting. Per-DSCP steering is what 'application-aware' means at the packet level: the SD-WAN reads the marking, honors it rather than remarking it, measures every available path continuously, and places each class on the path that serves it — re-evaluated in real time as path conditions change. Vendor sources: https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html | https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 20
THE COMPONENT STACK
Three components, three layers — frequently conflated
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
20
Component | Layer | Function | Representative vendors
SD-WAN overlay | L3 — Network | IPsec transport; path selection; QoS classification; DIA local breakout | Cisco Catalyst SD-WAN · VMware VeloCloud · Palo Alto
SASE SSE | L7 — Application | SWG, CASB, FWaaS, TLS inspection; TIC 3.0 security capabilities | Zscaler ZIA · Netskope SSE · Prisma Access
ZTNA | L7 — Application | Per-app micro-tunnels; device posture; least-privilege sessions | Zscaler ZPA · Netskope PA · Prisma Access ZTNA
Distinct products, both required: the SD-WAN overlay closes SC-8 (network-layer encryption on DIA) and SI-4 (transport telemetry). The SASE SSE stack closes AC-4, SC-7, SI-3, AU-2/AU-12, and CA-7. Neither substitutes for the other; both are required to satisfy TIC 3.0 and the controls in this book.
Vendor selection pending — all three components. Shortlists reflect FedRAMP authorization status at time of writing. Marketplace listings, procurement authority, and environment testing govern final selection; OIS participates in all three evaluations.
Notes: The telecommunications modernization requires three distinct components that operate at different layers and are frequently conflated in procurement conversations — this table is the disambiguation. The SD-WAN overlay at layer 3: IPsec encrypted transport, intelligent path selection, QoS traffic classification, and DIA local breakout — representative vendors Cisco Catalyst SD-WAN, VMware VeloCloud (Broadcom), Palo Alto SD-WAN. The SASE Secure Service Edge at layer 7: secure web gateway, CASB, firewall-as-a-service, SSL/TLS inspection — the TIC 3.0 security capabilities catalog made deliverable — representative vendors Zscaler Internet Access, Netskope SSE, Palo Alto Prisma Access. ZTNA, also layer 7: per-application micro-tunnels, device posture enforcement, least-privilege session access — Zscaler Private Access, Netskope Private Access, Prisma Access ZTNA. The grey panel carries the control mapping that makes 'both required' non-negotiable: the SD-WAN overlay closes SC-8 (network-layer encryption on DIA circuits) and SI-4 (application-layer telemetry on transport); the SASE SSE stack closes AC-4 (information flow enforcement), SC-7 (boundary protection), SI-3 (malware protection via SSL inspection), AU-2/AU-12 (per-session audit records), and CA-7 (continuous monitoring). Neither substitutes for the other. The amber panel is the procurement honesty the book carries as a callout: vendor selection is PENDING for all three components — the shortlists reflect FedRAMP authorization status and federal use-case alignment at time of writing, and agency procurement authority, current FedRAMP Marketplace listings, and environment-specific testing must inform final selection, with OIS participating in all three evaluations. Mechanism, not product — the doctrine slide from the series applies here in full. Vendor sources: https://www.cisa.gov/resources-tools/programs/trusted-internet-connections-tic | https://www.fedramp.gov/20x/ | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 21
THE COMPLIANCE HALF — CONTROLS
DIA is a pipe: what actually satisfies the NIST controls
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
21
Control | Requirement | What provides it
AC-4 | Information flow enforcement | CASB — application-layer identification
SC-7 | Boundary protection | SWG — application-layer inspection and malware scanning
SC-8 | Transmission confidentiality/integrity | SD-WAN IPsec tunnel — network-layer encryption
SI-3 | Malware protection | SWG — SSL inspection and malware scanning
SI-4 | System monitoring | AAN — application-layer telemetry, behavioral analysis
AU-12 | Audit record generation | AAN logging — user, device, app, action, data type, timestamp
CA-7 | Continuous monitoring | SASE stack — per-session identity, posture, access records
DIA enables; SASE and AAN achieve. DIA solves the G.114 latency problem — that is its entire contribution to compliance. A deployment that adds DIA without the control stack has better latency and the same compliance gaps.
Notes: The compliance half of the argument begins here. When a telecommunications modernization proposal says 'we will add DIA at field offices,' the technical response must be precise: DIA is a pipe. It solves the geographic hairpin problem. It does not solve any NIST control requirement. The table maps seven controls to what actually provides them: AC-4 information flow enforcement — the CASB, via application-layer identification; SC-7 boundary protection — the secure web gateway with application-layer inspection and malware scanning; SC-8 transmission confidentiality and integrity — the SD-WAN IPsec tunnel providing network-layer encryption; SI-3 malware protection — the SWG's SSL inspection; SI-4 system monitoring — AAN application-layer telemetry and behavioral analysis; AU-12 audit record generation — AAN logging with user, device, application, action, data type, and timestamp per record; CA-7 continuous monitoring — the SASE stack's per-session identity, posture, and access records. Notice the 'what provides it' column never says 'the circuit.' One closure-necessity argument worth voicing on SC-8: a DIA circuit carries traffic unencrypted at the network layer. SRTP protects the media payload of a call — but not the signaling, not the softphone HTTPS session metadata, and none of the non-voice traffic sharing the circuit; application-layer TLS covers no non-TLS flows at all. The only mechanism that encrypts ALL traffic on a DIA path regardless of application behavior is an IPsec overlay — SD-WAN. No configuration setting, scanner finding, or policy document closes SC-8 on a bare pipe. The red bar compresses the section: DIA enables; SASE and AAN achieve. Vendor sources: https://csrc.nist.gov/pubs/sp/800/53/r5/upd1/final | https://www.cisa.gov/resources-tools/programs/trusted-internet-connections-tic | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 22
THE COMPLIANCE HALF — POLICY
TIC 3.0: the policy that makes local breakout lawful
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
22
TIC 3.0 use case | Agency population | Traffic path governed | Where the PEP must be
Branch Office (Use Case E) | Field office agents on Connect + Teams Phone | Field office → local DIA → AWS .com / M365 GCC | At or near branch egress: SD-WAN edge + SASE services
Remote User (Use Case F) | Teleworking agents and staff | Home network → internet → cloud voice platforms | Cloud-delivered SASE PoP; ZTNA replacing VPN
The permissibility rule: TIC 3.0 (OMB M-19-26) replaced mandatory consolidation with a use-case model. Both use cases PERMIT traffic to leave without hairpinning through a TIC access point. Neither permits it to leave UNGOVERNED: the security-capabilities catalog must be satisfied at the distributed PEP — and the SASE stack is that PEP.
An ungoverned DIA circuit is not modernization; it is a finding. The bare circuit that fixes G.114 simultaneously deletes the SC-7 boundary the MPLS-to-TIC path did provide. With the SASE PEP in place, the same circuit is the TIC 3.0 target architecture. The difference is not the circuit — it is the control stack riding on it.
Notes: Physics explains why the agency NEEDS local breakout; it does not answer whether the agency MAY HAVE it. That is a policy question, and the policy is TIC 3.0. Under TIC 2.x, every byte of agency internet traffic egressed through a small number of consolidated access points — the architecture that created the hairpin. TIC 3.0 (OMB M-19-26) replaced mandatory consolidation with a use-case model: agencies may distribute internet egress, provided the protections the consolidated boundary used to provide are re-established at each distributed egress point — enumerated in the TIC 3.0 Security Capabilities Catalog, applied at the policy enforcement point governing each path. The two use cases governing agency voice: Branch Office (shorthand Use Case E elsewhere in the series) — field office agents on Connect and Teams Phone, traffic path field office → local DIA → AWS .com or M365 GCC, PEP at or near the branch egress as SD-WAN edge plus SASE services. Remote User (Use Case F) — teleworking agents and staff, home network → internet → cloud voice platforms, PEP as the cloud-delivered SASE PoP the user's traffic traverses, with ZTNA replacing VPN. The permissibility rule, stated formally: under TIC 3.0, DIA is permissible only when the security-capabilities catalog is satisfied at the distributed PEP — and the SASE stack IS that PEP. An agency that deploys it has not found a loophole around the TIC; it has implemented TIC 3.0 as designed. Also voice SC-7(7): split tunneling on remote devices is prohibited unless provisioned securely — and local breakout for voice is precisely a split tunnel; the distributed PEP is what provisions it securely. The red bar is the assessor's framing: an ungoverned DIA circuit is a finding; with the PEP it is the target architecture. The difference is not the circuit — it is the control stack riding on it. Vendor sources: https://www.cisa.gov/resources-tools/programs/trusted-internet-connections-tic | https://csrc.nist.gov/pubs/sp/800/207/final | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 23
THE COMPLIANCE HALF — BOUNDARY
Boundary documentation: what the SSP must say
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
23
Amazon Connect (.com)
SA-9: external service — identify Connect, its authorization, the specific exception, and data types
Call recordings in S3 on .com: access controls, KMS key management, lifecycle, AU-9 access logging
CRM/case-management API calls cross the boundary — the SSP data flow diagram must trace them
Agent federation (Entra ID → SAML/OIDC) is a cross-boundary credential flow — document it
The exception itself: reviewed at each ATO renewal, not a permanent waiver
Teams Phone (GCC Moderate)
Signaling, voicemail, call history, and policy all inside the GCC boundary — no new exception needed
The PSTN interconnect is a boundary crossing by definition: the PSTN is a public network
The SBC handles the crossing point — its configuration must be documented in the SSP as a boundary interface
Recording storage is GCC-boundary-compliant
ConMon evidence: voice quality, E911 test records, SBC documentation
Notes: The boundary documentation each platform requires — the AO-facing slide. Amazon Connect on .com, five obligations: SA-9 documentation identifying Connect as an external information system service, its FedRAMP authorization status, the specific authorized exception, and the data types involved — voice audio, call recordings, call metadata, citizen interaction logs. Call recordings stored in S3 on AWS commercial: access controls, KMS encryption key management, and data lifecycle policies documented; recordings containing PII classified accordingly, with access logging satisfying AU-9. CRM and case management integration: API calls between Connect contact flows and agency systems cross the .com boundary, and the SSP data flow diagram must trace them. Agent authentication federation: agents authenticate via the agency IdP — Entra ID in GCC Moderate — and that SAML/OIDC federation is a cross-boundary credential flow that must be documented. And the exception itself: reviewed at each ATO renewal — a time-bounded, condition-bounded authorization requiring active maintenance, not a permanent waiver. Teams Phone is the cleaner column: call signaling, voicemail storage, call history, and user policy management all operate inside the GCC boundary — no new exception. The one boundary crossing is definitional: the PSTN is a public network, so the PSTN interconnect via Direct Routing SBC or Calling Plans crosses the boundary, and the SBC handles the crossing point — its configuration must be documented in the SSP as a boundary interface. Recording storage is GCC-boundary-compliant, and the agency's ConMon evidence obligations are voice quality monitoring, E911 testing records, and SBC boundary documentation — which the 20x slide two ahead converts into machine-readable KSI terms. Vendor sources: https://aws.amazon.com/compliance/fedramp/ | https://learn.microsoft.com/en-us/office365/servicedescriptions/office-365-platform-service-description/office-365-us-government/gcc | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 24
TWO PLATFORMS, ONE ARCHITECTURE
Complementary, not competing — and identical where it matters
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
24
Dimension | Amazon Connect (N8NN) | Teams Phone (internal UC)
Primary function | Citizen-facing inbound contact center | Employee-to-employee and PSTN calling
Users | Contact center agents, supervisors | All agency employees
IVR / routing | Contact flows, skills-based routing, queuing | Auto attendants and call queues
Authorization | FedRAMP Moderate (.com by specific exception) | FedRAMP Moderate (M365 GCC Moderate)
Voice protocol | WebRTC / RTP / DSCP EF | WebRTC / RTP / DSCP EF
Network requirement | <75 ms · <30 ms jitter · <1% loss | IDENTICAL
SD-WAN solution | Local breakout · EF steering · multipath · FEC | IDENTICAL
The most operationally significant rows are the last two: these are not separate network projects. One network modernization enables both platforms.
Notes: The comparison table, condensed from the book's full version — and deliberately ordered so the differences come first and the identities come last. The platforms are complementary, not competing: Amazon Connect is the citizen-facing inbound contact center — high-volume inbound with thousands of concurrent calls at peak, sophisticated contact flows, skills-based routing, Contact Lens transcription and sentiment analytics, the browser-based Contact Control Panel; Teams Phone is internal unified communications — employee-to-employee and PSTN calling for all agency employees, auto attendants and call queues at standard enterprise PBX volume, in the Teams client. Authorization differs in mechanism: Connect at FedRAMP Moderate on .com by specific agency exception, Teams Phone at FedRAMP Moderate inside M365 GCC Moderate — both at the Moderate baseline. Then the teal rows, where the table stops contrasting: the voice protocol row is already identical — WebRTC, RTP, DSCP EF on both platforms. The network requirement row: under 75 ms one-way, under 30 ms jitter, under 1% loss — IDENTICAL. The SD-WAN solution row: local breakout, DSCP EF steering, active-active multipath, FEC — IDENTICAL. The closing bar states the consequence the whole deck has been building: the SD-WAN investment that enables Amazon Connect to meet G.114 from all field office locations is the same investment that enables Teams Phone to deliver acceptable call quality. These are not separate network projects — one network modernization enables both platforms, which is why the implementation roadmap that follows sequences the network FIRST and both platforms behind it. Vendor sources: https://aws.amazon.com/connect/ | https://learn.microsoft.com/en-us/microsoftteams/what-is-phone-system-in-office-365 | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 25
THE COMPLIANCE CLOCK — 20X FOR TELECOM
FedRAMP 20x: what continuous monitoring means for voice
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
25
Date | Event | Telecom implication
Jul 28, 2026 | FedRAMP Ready submissions cease | No new Ready pathway for Connect or SBC vendors
Aug 3, 2026 | Class A pipeline opens | Evaluate whether Connect .com falls under Class A
Aug 31, 2026 | Class B and C open | Multi-platform unified comms likely Class B or C
Jan 1, 2027 | Consolidated Rules mandatory | All ConMon evidence must align to 20x KSI format
Jun 11, 2027 | No new Rev5 certifications | Plan for 20x pathway on next ATO cycle
KSI evidence for voice: Connect call audit logs (AU-12) as structured, queryable records; Entra ID → Connect SAML assertions as verifiable authentication telemetry (IA-8); boundary-crossing API calls captured machine-readably (SA-9); the .com exception maintained in a 20x-compatible continuous-review format. Teams Phone: MOS floor per location, E911 test records, SBC logs to the SIEM.
SD-WAN as 20x evidence generator: every path decision, jitter measurement, and FEC activation is a logged, queryable event. The network investment IS the compliance evidence generator. Not separate investments.
Notes: FedRAMP published its Consolidated Rules for 2026 on June 25, 2026, and this slide reads the timeline specifically for telecommunications. July 28, 2026: FedRAMP Ready submissions cease — no new Ready pathway for Connect or SBC vendors. August 3: the Class A pipeline opens — evaluate whether Connect .com falls under Class A. August 31: Class B and C open — a multi-platform unified communications offering likely lands in Class B or C. January 1, 2027 — the amber row — the Consolidated Rules become mandatory: ALL continuous monitoring evidence must align to the 20x KSI format. June 11, 2027: no new Rev5 certifications — plan for the 20x pathway on the next ATO cycle. What 20x means for Amazon Connect: 20x replaces periodic evidence assembly with continuously verified Key Security Indicators in machine-readable format. Call audit logs under AU-12 — every agent session, call recording access, and contact flow execution as structured, queryable records, not archived log files. Federated authentication events under IA-8 — Entra ID to Amazon Connect SAML assertions producing KSI-verifiable authentication telemetry. Boundary traffic under SA-9 — API calls crossing the .com boundary captured machine-readably. And the ATO exception itself maintained in a format compatible with 20x continuous review rather than point-in-time SSP snapshots. For Teams Phone, the agency's evidence — voice quality monitoring against the MOS floor per location, E911 testing records, SBC boundary documentation — must align to the same KSI format. The teal bar is the argument that closes budget discussions: the SD-WAN overlay that solves G.114 also GENERATES the machine-readable evidence 20x requires — every path decision, jitter measurement, and FEC activation is a logged, queryable event. The network investment and the compliance evidence generator are the same line item. Vendor sources: https://www.fedramp.gov/20x/ | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd

## Slide 26
THE FEDERAL COMPLIANCE CLOCK
Every deadline running against these controls
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
26
Aug 3 / 31, 2026 FedRAMP 20x opens — Class A, then Class B + C: the GCC Moderate window
Aug 7, 2026 BOD 26-04: agency vulnerability-management policies must support risk-based remediation
Sep 21, 2026 FIPS 140-2 certificates move to NIST's Historical List — verify FIPS 140-3 tracking (SC-13)
Dec 7, 2026 BOD 26-04 remediation timelines in force + FedRAMP VDR/VER mandatory (SBOM + vendor disclosure)
Jan 1, 2027 FedRAMP CR26 mandatory for all · CNSA 2.0 acquisition gate (NSS-scoped; civilian PQC follows)
Jun 11, 2027 No new Rev5 certifications accepted
~Aug 2027 Next scheduled NIST 800-53 release — 5.2.0 (Aug 2025) already added SA-15(13), SA-24, SI-2(7)
2030 / 2035 Quantum-vulnerable cryptography deprecated, then prohibited — M-23-02 inventories run to the horizon
SSOT for federal dates: the Federal AAN / ConMon Gap Roadmap (verified 2026-07-07). Already in force: M-21-31 logging, M-21-07 IPv6, M-22-09 Zero Trust (continued by M-24-14 / M-25-04), BOD 25-01 SCuBA.
Notes: The federal compliance clock — the series-standard slide; the fully-sourced version with the elapsed baseline lives in the Federal AAN / ConMon Gap Roadmap, the series' single source of truth for dates (verified 2026-07-07). Walk the rows: August 3 and 31, 2026 — FedRAMP 20x submission windows open, Class A first, then Class B and C, which is the GCC Moderate window (marketplace listings opened July 6; FedRAMP Ready went legacy July 28; temporary Rev5 conversion paths opened August 10). August 7, 2026 — BOD 26-04 (issued June 10, 2026) requires agency vulnerability-management policies to support risk-based remediation under its four-variable model: exposure, KEV listing, exploit automatability, and technical impact. September 21, 2026 — every FIPS 140-2 certificate moves to NIST's Historical List, ending new procurement reliance on 140-2-only validated modules. December 7, 2026 — BOD 26-04's remediation timelines take force AND FedRAMP's Vulnerability Detection and Response / Vulnerability Evaluation and Reporting rules become mandatory: SBOM plus vendor disclosure. January 1, 2027 — the Consolidated Rules become mandatory for all FedRAMP systems, and CNSA 2.0's acquisition gate opens for National Security Systems (NSS-scoped; the civilian trajectory follows via M-23-02). June 11, 2027 — no new Rev5 certifications. Around August 2027 — the next scheduled NIST 800-53 release on the two-year cadence; Release 5.2.0 (August 27, 2025) already added SA-15(13), SA-24, and SI-2(7), not yet mapped in the series' Parts 11/15 closure tables — a tracked action item. 2030/2035 — quantum-vulnerable cryptography deprecated then prohibited; M-23-02's annual crypto inventories run to that horizon. For Book 06 specifically, the January 1, 2027 row is the binding one: it is why Phase 4 of the roadmap carries 20x KSI alignment as an explicit work item, not an aspiration. Vendor sources: https://www.fedramp.gov/20x/ | https://www.cisa.gov/news-events/directives/bod-26-04-prioritizing-security-updates-based-risk | https://csrc.nist.gov/News/2025/nist-releases-revision-to-sp-800-53-controls | uiao repo: inbox/Application Aware Networking/federal-aan-conmon-gap-roadmap.md

## Slide 27
IMPLEMENTATION ROADMAP — PHASE 1 (MONTHS 1–3)
Network foundation — no migration before validation
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
27
Phase 1
Months 1–3
Phase 2
Months 2–5
Phase 3
Months 4–8
Phase 4
Months 6+
PREREQUISITE for everything: no office goes live on either platform until its network is G.114-validated
Deploy SD-WAN at all field offices with agents or significant phone populations; configure local breakout for AWS .com and M365 GCC endpoints
Per-DSCP steering: EF → lowest-latency path; HTTPS → highest-throughput. FEC on any path with loss ≥0.5%
Verify direct outbound UDP without hairpin or deep-inspection delay; size EF capacity: max hybrid agents × 200 Kbps
Measure and document G.114 compliance at each agent location before Phase 2
Notes: Build 1 of 4 — the network foundation, and the roadmap's governing rule stated as the first bullet: no telecommunications migration before network validation. Voice quality failures discovered after a contact center or PBX migration are dramatically more expensive to remediate than network investments made before migration — so no field office goes live on Amazon Connect or Teams Phone until its network foundation is validated against G.114. Validation is defined concretely: measure actual one-way latency, jitter, and packet loss from each agent workstation to AWS us-west-2 and to the Microsoft GCC edge, with local breakout active, and confirm all three parameters within specification. The work items: deploy SD-WAN at every field office with contact center agents or significant phone populations; configure local internet breakout for the Amazon Connect .com AWS IP ranges and FQDNs and the Microsoft 365 GCC endpoints; enable per-DSCP steering — DSCP EF to the lowest-latency path, standard HTTPS to the highest-throughput path; enable FEC on any path with measured loss at or above 0.5%; verify direct outbound UDP to Connect and GCC endpoints without hairpin or deep-inspection delay; size the DSCP EF capacity for peak hybrid agent load at maximum concurrent hybrid agents times 200 Kbps; and close the phase by measuring and documenting G.114 compliance at each agent location — the dated, per-location record that gates Phase 2. Vendor sources: uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd | https://docs.aws.amazon.com/connect/latest/adminguide/ccp-networking.html

## Slide 28
IMPLEMENTATION ROADMAP — PHASE 2 (MONTHS 2–5)
Amazon Connect deployment — on a validated network
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
28
Phase 1
Months 1–3
Phase 2
Months 2–5
Phase 3
Months 4–8
Phase 4
Months 6+
Confirm the .com exception is current in the ATO; update SSP SA-9 with current architecture
Design contact flows replicating and improving current N8NN IVR routing
Agent authentication via IdP federation: Entra ID (GCC Moderate) → Amazon Connect
Pilot with a single queue and agent cohort; measure MOS, jitter, loss from pilot locations
Validate the recording pipeline to S3 (KMS, access controls, AU-9) and CRM integration; document data flows in the SSP
Notes: Build 2 of 4 — Amazon Connect deployment, overlapping Phase 1 from month 2 because contact flow design and boundary paperwork do not need the network finished — but no agent cohort goes live at an office that has not passed its Phase 1 validation. The work items: confirm the .com exception is current in the ATO and update the SSP SA-9 documentation for Amazon Connect with the current architecture — the boundary obligations from earlier in the deck become concrete deliverables here. Design and build contact flows replicating and improving the current N8NN IVR routing — the improvement opportunity is real: skills-based routing and Contact Lens analytics exceed what the legacy platform offered. Configure agent authentication via IdP federation — Entra ID in GCC Moderate asserting to Amazon Connect over SAML — which is itself a documented cross-boundary credential flow. Pilot with a single queue and a single agent cohort, measuring MOS, jitter, and loss from the pilot locations against the Phase 1 baseline — the pilot is the E-model working as an acceptance gate. Validate the call recording pipeline to S3: KMS key management, access controls, AU-9 access logging; and validate the CRM/case-management integration, documenting the data flow in the SSP. Every item here produces either a working capability or an authorization artifact — by design. Vendor sources: uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd | https://aws.amazon.com/connect/

## Slide 29
IMPLEMENTATION ROADMAP — PHASE 3 (MONTHS 4–8)
Teams Phone deployment — tranche by tranche
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
29
Phase 1
Months 1–3
Phase 2
Months 2–5
Phase 3
Months 4–8
Phase 4
Months 6+
Confirm GCC tenant feature availability: Calling Plans, voicemail transcription, mobile calling
Deploy and configure the SBC (on-prem or cloud); validate Microsoft certification and FedRAMP authorization
E911: dispatchable location per office, PSAP connectivity verified, tests documented — before go-live
Inventory legacy PBX numbers: voice, fax, emergency, or special service
Build Call Queues + Auto Attendants from legacy hunt groups; port in geographic tranches with parallel PBX operation
Notes: Build 3 of 4 — Teams Phone, months 4 through 8, tranche by tranche. First, confirm Teams Phone feature availability in the agency's GCC tenant — Calling Plans availability, voicemail transcription, mobile calling — because GCC feature parity is a moving target and commitments must rest on confirmed capability, not commercial documentation. Second, deploy and configure the SBC — on-premises or cloud-hosted per the earlier decision — validating both its Microsoft Direct Routing certification and, for a cloud SBC, its FedRAMP authorization on the Marketplace. Third, E911: configure dispatchable location for every office location, verify PSAP connectivity, and document the testing — the four-step legal gate from the E911 slide, executed per location BEFORE that location goes live. Fourth, inventory legacy PBX numbers and classify each as voice, fax, emergency, or special service — the classification that keeps fax lines and elevator phones from being discovered mid-cutover. Fifth, build Teams Call Queues and Auto Attendants replicating the legacy hunt groups and menus, then port numbers in geographic tranches while maintaining parallel PBX operation through each tranche — every tranche bounded, reversible, and validated before the next begins. The month-8 milestone is PBX decommission at completed sites; the freeze-window and rollback rules from the series' governance gates apply to every tranche. Vendor sources: uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd | https://learn.microsoft.com/en-us/microsoftteams/direct-routing-landing-page

## Slide 30
IMPLEMENTATION ROADMAP — PHASE 4 (MONTHS 6+)
Continuous monitoring and 20x alignment
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
30
Phase 1
Months 1–3
Phase 2
Months 2–5
Phase 3
Months 4–8
Phase 4
Months 6+
SD-WAN dashboards surface G.114 violations by location BEFORE they become citizen complaints
Connect Call Analytics → agency SIEM for AU-12 continuous monitoring
MOS floor SLA ≥4.0 per agent location, with alerting on sustained drops
Review the .com exception at each ATO renewal; re-evaluate whether .us capability gaps have closed
20x (mandatory Jan 1, 2027): SD-WAN telemetry in machine-readable JSON; Connect logs, auth events, and SBC logs in structured KSI format
Notes: Build 4 of 4 — the phase that never ends, starting month 6 and running as standing operations. Instrument the SD-WAN dashboards to surface G.114 violations by location BEFORE they become citizen complaints — the monitoring posture inverts from reactive (complaint → investigation) to proactive (dashboard → fix → no complaint). Integrate Amazon Connect Call Analytics with the agency SIEM for AU-12 continuous monitoring — call records as structured security telemetry, not just contact center reporting. Establish the MOS floor SLA: at or above 4.0 per agent location — per location, not fleet average — with alerting when sustained MOS drops below threshold. Review the Amazon Connect .com exception at each ATO renewal and re-evaluate whether the .us capability gaps that justified it have been resolved — the exception is condition-bounded, and the condition is re-tested, not assumed. And the FedRAMP 20x alignment work, mandatory January 1, 2027: configure SD-WAN telemetry exports in machine-readable JSON; ensure Connect audit logs, authentication events, and boundary-crossing records meet the structured KSI format requirements; validate that SBC event logs feed the SIEM in queryable format. The through-line to close on: every operational item in this phase doubles as authorization evidence — the voice quality program and the ConMon program are the same program, which is the 20x design intent arriving in telecom form. Vendor sources: uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd | https://www.fedramp.gov/20x/

## Slide 31
WHERE THIS LEAVES US
One problem, one solution, two platforms — and what to decide
Federal AAN — Book 06 Telecom Modernization · CSI Team Draft — Internal · FedRAMP Moderate · Date Code 2026-07-07 15:57 ET
31
The physics Voice has a pass/fail threshold — G.114's 150 ms ceiling leaves ~75 ms for the network. The MPLS hairpin spends it before the call begins; local breakout returns it. Jitter <30 ms, loss <1% complete the spec.
The platforms Amazon Connect (.com by maintained exception) carries the citizen; Teams Phone (GCC Moderate) replaces the PBX. Identical network requirements, identical SD-WAN solution — one investment, made once.
The compliance DIA is a pipe; the SASE stack is the TIC 3.0 PEP that makes breakout lawful and the controls real. The same SD-WAN telemetry is the machine-readable evidence FedRAMP 20x makes mandatory Jan 1, 2027.
Asks for OIS + CIO Office: adopt the network-first sequencing (no migration before G.114 validation) · decide the SBC model (on-prem vs. FedRAMP-authorized cloud SBC) · confirm Calling Plans availability in the GCC tenant · fund the SASE stack with the DIA circuits, not after them · schedule the .com exception re-evaluation into every ATO renewal.
Notes: Closing slide — the book compressed to three bars and five asks. The physics: voice quality has a pass/fail threshold defined by international standard — G.114's 150 ms one-way ceiling leaves roughly 75 ms for the network; the MPLS hairpin spends that budget before the call begins, local breakout returns it, and jitter under 30 ms plus loss under 1% complete the specification. The platforms: Amazon Connect on .com by a maintained, condition-bounded exception carries the citizen-facing N8NN; Teams Phone inside GCC Moderate replaces the legacy PBX with no new boundary complications; their network requirements are identical and their network solution is identical — one investment, made once. The compliance: DIA is a pipe — the SASE stack is the TIC 3.0 policy enforcement point that makes local breakout lawful and the NIST controls real; and the same SD-WAN telemetry that proves G.114 compliance is the machine-readable KSI evidence FedRAMP 20x makes mandatory on January 1, 2027. The five asks: adopt network-first sequencing — no office migrates to either platform before its G.114 validation, which is the single rule that prevents the expensive failure mode; decide the SBC deployment model, on-premises versus a FedRAMP-authorized cloud SBC, because it gates Phase 3 procurement; confirm Calling Plans availability in the agency's GCC tenant before the Direct Routing commitment is final; fund the SASE stack WITH the DIA circuits, not after them — an ungoverned circuit is a finding, not a modernization; and schedule the .com exception re-evaluation into every ATO renewal as a standing ConMon item. All scoped to FedRAMP Moderate. The Date Code identifies this version; newest code wins. Vendor sources: https://www.itu.int/rec/T-REC-G.114 | https://www.fedramp.gov/20x/ | uiao repo: inbox/Application Aware Networking/Book_06_FedAAN_Federal_Telecommunications_Modernization.qmd